## Slide 1: Representing Integer Data

## Slide 2: Ranges for Data Formats
No. of bits | Binary | BCD | ASCII
1 | 0 – 1 |  | 
2 | 0 – 3 |  | 
3 | 0 – 7 |  | 
4 | 0 – 15 | 0 – 9 | 
5 | 0 – 31 |  | 
6 | 0 – 63 |  | 
7 | 0 – 127 |  | 
8 | 0 – 255 | 0 – 99 | 0 – 9
9 | 0 – 511 |  | 
16 | 0 - 65,535 | 0 – 9999 | 0 – 99
24 | 0 – 16,777,215 | 0 – 999999 | 0 – 999
Etc. |  |  | 

## Slide 3: In General (binary)
No. of bits | Binary | 
 | Min | Max
n | 0 | 2n - 1

## Slide 4: Signed Integers
Previous examples were for “unsigned integers” (positive values only!)
Must also have a mechanism to represent “signed integers” (positive and negative values!)
E.g., -510 = ?2
Two common schemes: sign-magnitude and twos complement

## Slide 5: Sign-Magnitude
Extra bit on left to represent sign
  0 = positive value
  1 = negative value
E.g., 6-bit sign-magnitude representation of +5 and –5:
+5: 0 0 0 1 0 1
+ve
5
-5: 1 0 0 1 0 1
-ve
5

## Slide 6: Ranges (revisited)
No. of bits | Binary |  |  | 
 | Unsigned |  | Sign-magnitude | 
 | Min | Max | Min | Max
1 | 0 | 1 |  | 
2 | 0 | 3 | -1 | 1
3 | 0 | 7 | -3 | 3
4 | 0 | 15 | -7 | 7
5 | 0 | 31 | -15 | 15
6 | 0 | 63 | -31 | 31
Etc. |  |  |  | 

## Slide 7: In General (revisited)
No. of bits | Binary |  |  | 
 | Unsigned |  | Sign-magnitude | 
 | Min | Max | Min | Max
n | 0 | 2n - 1 | -(2n-1 - 1) | 2n-1 - 1

## Slide 8: Difficulties with Sign-Magnitude
Two representations of zero
  Using 6-bit sign-magnitude…
    0: 000000
    0: 100000
Arithmetic is awkward!

## Slide 9: Exercises – Complementary Notations
What is the 3-digit 10’s complement of 247?
  Answer:
What is the 3-digit 10’s complement of 17?
  Answer:
777 is a 10’s complement representation of what decimal value?
  Answer:

## Slide 10: Exercises – Complementary Notations
What is the 3-digit 10’s complement of 247?
  Answer: 753
What is the 3-digit 10’s complement of 17?
  Answer: 983
777 is a 10’s complement representation of what decimal value?
  Answer: 223
Answer

## Slide 11: Twos Complement
Most common scheme of representing negative numbers in computers
Affords natural arithmetic (no special rules!)
To represent a negative number in 2’s complement notation…
    Decide upon the number of bits (n)
    Find the binary representation of the +ve value in n-bits
    Flip all the bits (change 1’s to 0’s and vice versa)
    Add 1

## Slide 12: Twos Complement Example
Represent -5 in binary using 2’s complement notation
    Decide on the number of bits
    Find the binary representation of the +ve value in 6 bits
    Flip all the bits
    Add 1
6 (for example)
111010
111010
+ 1
111011
-5
000101
+5

## Slide 13: Sign Bit
In 2’s complement notation, the MSB is the sign bit (as with sign-magnitude notation)
  0 = positive value
  1 = negative value
-5: 1 1 1 0 1 1
-ve
+5: 0 0 0 1 0 1
+ve
5
? (previous slide)

## Slide 14: “Complementary” Notation
Conversions between positive and negative numbers are easy
For binary (base 2)…
+ve
-ve
2’s C
2’s C

## Slide 15: Example
+5
2’s C
-5
2’s C
+5
0 0 0 1 0 1
1 1 1 0 1 0 + 1
1 1 1 0 1 1
0 0 0 1 0 0 + 1
0 0 0 1 0 1

## Slide 16: Exercise – 2’s C conversions
What is -20 expressed as an 8-bit binary number in 2’s complement notation?
  Answer:
1100011 is a 7-bit binary number in 2’s complement notation. What is the decimal value?
  Answer:

## Slide 17: Exercise – 2’s C conversions
What is -20 expressed as an 8-bit binary number in 2’s complement notation?
  Answer: 1101100
1100011 is a 7-bit binary number in 2’s complement notation. What is the decimal value?
  Answer: -29
Answer

## Slide 18: 2’s Complement Addition
Easy
No special rules
Just add

## Slide 19: What is -5 plus +5?
Zero, of course, but let’s see
-5: 10000101 +5: +00000101 10001010
Sign-magnitude
-5: 11111011 +5: +00000101 00000000
Twos-complement
1
1
1
1
1
1
1
1

## Slide 20: 2’s Complement Subtraction
Easy
No special rules
Just subtract, well … actually … just add!
A – B = A + (-B)
add
2’s complement of B

## Slide 21: What is 10 subtract 3?
7, of course, but…
Let’s do it (we’ll use 6-bit values)
10 – 3 = 10 + (-3) = 7
001010 +111101 000111
+3: 000011
1s C: 111100 +1: 1 -3: 111101

## Slide 22: What is 10 subtract -3?
13, of course, but…
Let’s do it (we’ll use 6-bit values)
10 – (-3) = 10 + (-(-3)) = 13
001010 +000011 001101
-3: 111101
1s C: 000010 +1: 1 +3: 000011
(-(-3)) = 3

## Slide 23: Thank You