## Slide 1: Instruction Format

## Slide 2: Introduction
Computer Program is a set of instruction to solve a task
Control Unit (CU) interpret the instruction code and send signal to ALU, Memory
Instruction Format define the layout of the bits of an instruction
Computer has variety of instruction code format

## Slide 3: Instruction Fields
Operation Field | Mode | Address
Operation Field: Specifies the operation to be performed (ADD, STORE, MUL etc…)
Address Field: Contain the location of operands Register/ Memory.
Mode: Specified how operand is access from memory (Address Mode)

## Slide 4: Instruction Format
Four Types of Instruction formats
  Three Address Instructions
  Two Address Instructions
  One Address Instructions
  Zero Address Instructions

## Slide 5: Three Address Instructions
OP code | Destination Address | Source Address | Source Address | Mode
It contain 3 Address
Destination address for Result, other two address for Operands
Program size is small because here Instruction size is large

## Slide 6: Three Address Instructions
Assembly Code for Z = (A+B) * (C+D)
ADD R1, A, B R1 = M[A] + M[B]
ADD R2, C, D R2 = M[C] + M[D]
MUL Z, R1, R2 M[Z] = R1 * R2

## Slide 7: Two Address Instructions
OP code | Destination Address | Source Address | Mode
Most commonly used in Commercial computers
Two Address fields are used.
Destination address for Result and also act as source
One source address for Operands

## Slide 8: Two Address Instructions
Assembly Code for Z = (A+B) * (C+D)
MOV R1, A R1 = M[A]
ADD R1,B R1 = R1 + M[B]
MOV R2, C R2 = M[C]
ADD R2, D R2 = R2 + M[D]
MUL R1, R2 R1 = R1 * R2
MOV Z, R1 M[Z] = R1

## Slide 9: One Address Instructions
OP code | Source/ Operand Address | Mode
Accumulator (AC) register used for data manipulation
So one operand in AC register and second in Memory / Register.
CPU is know one operand is store in AC register So no need to mention it.

## Slide 10: One Address Instructions
Assembly Code for Z = (A+B) * (C+D)
LOAD A AC = M[A]
ADD B AC = AC + M[B]
STORE T M[T] = AC
LOAD C AC = M[C]
ADD D AC = AC + M[D]
MUL T AC = AC * M[T]
STORE Z M[Z] = AC

## Slide 11: Zero Address Instructions
Here no any address field used for Instructions (ADD, SUB, MUL etc…)
Stack organized computer used this Instruction format
PUSH and POP instruction need operand address field

## Slide 12: One Address Instructions
Assembly Code for Z = (A+B) * (C+D)
Postfix : AB+ CD+ *
PUSH A TOS = A
PUSH B TOS = B
ADD TOS = A + B
PUSH C TOS = C
PUSH D TOS = D
ADD TOS = C+D
MUL TOS = (A+B) * (C+D)
POP Z M[Z] = TOS

## Slide 13: Thank You